## Slide 1
The Republic of the Union of Myanmar
Ministry of Electric Power
Electricity Supply Enterprise
Mon State Office
Priorities and Detailed Description of Electrification Plan
For Mon State
Dated -21.Oct.2015

## Slide 2
 | As Per DE Idea after discussion with Local government
 | The following factor are agreed to perform and Implement after discussion with chief minister (Mon state)
 | - To be performed priority the villages, which have along the main road.
 | - The villages within 2 miles from National Grid Line.
 | - To be performed priority villages having households more them 100 and above.
 | - To be explain the public of villages to construct the low voltage line by local fund.
 | - And them ,the remain villages will be implemented continuously by National Electrification plan.
 | - ESE (Mon state)will implement the work done under management MOEP coordination especially with local Government.

## Slide 3
Priority Electrification Project List for Mon State
No | District | Township | Nos of Village | Remark
1 | Mawlamyine | Mawlamyine | 2 | Within 2 miles Distance from existing grid Line
 |  | Mudon | 3 | ။
 |  | Thanbhyu zayat | 12 | ။
 |  | Kyaitmayaw | 12 | ။
2 | Thaton | Thaton | 20 | ။
 |  | KyaitHto | 5 | ။
 |  | Paung | 6 | ။
 |  | Belin | 20 | According to Replace with 33/11kV, 5 MVA Transformer To 33/11kV, 10 MVA Transformer
 |  | Total | 80 | 

## Slide 4
The additional electrification statement due to newly and upgrading 33/11kV substation and related power line for Mon State
Sr No | Township | To Be Constructed |  |  | The effective area (within 2 Miles) |  |  | Estimated Cost (millon kyats) |  | 
 |  | Substation | 66 kV Line (mile) | 33 kV Line (mile) | Total Vill(ages (Nos) | Total Household (Nos) | Total Population (Nos) | Material cost | Instruction cost | Total cost
1 | Belin | Upgrade 33/11kV 5MVA To 10 MVA | - | - | 20 | 2101 | 11882 | 706 | 14 | 720
Total |  | 1 | - | - | 20 | 2101 | 11882 | 706 | 14 | 720

## Slide 5
No | District | No of Village To be Electrif- ied | No of House | House hold | Popul-ation | To be constructed |  |  |  |  |  |  |  |  |  |  | Estima- ted cost (Mil Kyates) | Task by regional | 
 |  |  |  |  |  | Cost for 11 kV Line |  |  |  |  | 11/0.4 kV Transformer |  |  |  |  |  |  | 400 V Lines (Miles) | Estimated cost (Mil Kyates)
 |  |  |  |  |  | Mile | Materi al Cost | Transport Cost | Constr uc tion Cost | Total | KVA | No | Material Cost | Transport Cost | Construc tion Cost | Total |  |  | 
1 | Mawlamyine | 29 | 5450 | 5804 | 32405 | 26.49 | 664.98 | 36.16 | 106.54 | 807.68 | 4370 | 34 | 448.36 | 12.51 | 28.56 | 489.44 | 1297.12 | 30.34 | 1430.02
2 | Thaton | 51 | 6995 | 7291 | 39804 | 38.66 | 970.48 | 52.77 | 155.49 | 1178.74 | 6710 | 47 | 643.56 | 17.29 | 39.48 | 700.34 | 1879.08 | 43.35 | 2043.22
 | Total | 80 | 12445 | 13095 | 72209 | 65.15 | 1635.46 | 88.93 | 262.03 | 1986.42 | 11080 | 81 | 1091.92 | 29.81 | 68.04 | 1189.77 | 3176.19 | 73.69 | 3473.23
Detailed Electrification Plan for Mon State (Within 2 miles from Existing 11 kV Distribution Line)

## Slide 6
Electrification Plan for Villages of Mon State
(Within 2 miles from Existing 11 kV Distribution Line)
To be Constructed
11 kV Distribution Line 65.15miles
400 V Distribution Line 73.69 miles
11/0.4 kV Distribution Transformer 81Nos
33/11kV Main Transformer 1 Nos
Mon State Territory
No. of Villages - 80 Nos
Household - 13095
Estimated Cost - 3176.195
(mil kyats)
Thaton District
No. of Villages - 51 Nos
Household - 7291
Estimated Cost - 1879.08
(mil kyats)
Mawlamyine District
No. of Villages - 29Nos
Household - 5804 Estimated Cost - 1297.116
(mil kyats)

## Slide 7
Detailed Electrification Plan for Mawlamyine District
(Within 2 miles from Existing 11 kV Distribution Line)
No | Town ship | No of Village To be Electrifi- ed | No of House | House hold | Popula tion | To be constructed |  |  |  |  |  |  |  |  |  |  | Estimated cost (Mil Kyates) | Task by regional | 
 |  |  |  |  |  | Cost for 11 kV Line |  |  |  |  | 11/0.4 kV Transformer |  |  |  |  |  |  | 400 V Lines (Miles) | Estimated cost (Mil Kyates)
 |  |  |  |  |  | Mile | Materi al Cost | Transport Cost | Constr uc tion Cost | Total | KVA | No | Material Cost | Transport Cost | Construc tion Cost | Total |  |  | 
1 | Mawlamyine | 2 | 190 | 215 | 614 | 1.91 | 47.947 | 2.607 | 7.682 | 58.236 | 300 | 2 | 28.078 | 0.736 | 1.680 | 30.494 | 88.730 | 2.17 | 102.279
2 | Mudon | 3 | 1277 | 1277 | 6693 | 1.72 | 43.177 | 2.348 | 6.918 | 52.443 | 760 | 4 | 60.392 | 1.472 | 3.360 | 65.224 | 117.667 | 7 | 329.931
3 | Thanbyuzayat | 12 | 2133 | 2401 | 12510 | 11.02 | 276.635 | 15.042 | 44.322 | 336.000 | 1810 | 14 | 186.803 | 5.152 | 11.760 | 203.715 | 539.715 | 11.57 | 545.329
4 | Kyaik mayaw | 12 | 1850 | 1911 | 12588 | 11.84 | 297.220 | 16.162 | 47.620 | 361.002 | 1500 | 14 | 173.090 | 5.152 | 11.760 | 190.002 | 551.004 | 9.6 | 452.477
Total |  | 29 | 5450 | 5804 | 32405 | 26.49 | 664.979 | 36.159 | 106.542 | 807.681 | 4370 | 34 | 448.363 | 12.512 | 28.56 | 489.435 | 1297.116 | 30.34 | 1430.016

## Slide 8
Mawlamyine District
No. of Villages - 29 Nos
Household - 5804
Estimated Cost - 1297.116
(mil kyats)
Mudon Township
No. of Villages - 3 Nos
Household - 1277 Estimated Cost - 117.667
(mil kyats)
Kyaitmayaw Township
No. of Villages - 12 Nos
Household - 1911 Estimated Cost - 551.004
(mil kyats)
Mawlamyine Township
No. of Villages - 2 Nos
Househld - 215 Estimated Cost 88.730
(mil kyats)
Thanphyuzayat Township
No. of Villages - 12 Nos
Household - 2401 Estimated Cost - 539.715
(mil kyats)
Electrification Plan for Villages of Mawlamyine District
(Within 2 miles from Existing 11 kV Distribution Line)

## Slide 9
Detailed Electrification Plan for Thaton District
(Within 2 miles from Existing 11 kV Distribution Line)
No | Town ship | No of Village To be Electrif- ied | No of House | House hold | Popula tion | To be constructed |  |  |  |  |  |  |  |  |  |  | Estimated cost (Mil Kyates) | Task by regional | 
 |  |  |  |  |  | Cost for 11 kV Line |  |  |  |  | 11/0.4 kV Transformer |  |  |  |  |  |  | 400 V Lines (Miles) | Estimated cost (Mil Kyates)
 |  |  |  |  |  | Mile | Materi al Cost | Transport Cost | Constr uc tion Cost | Total | KVA | No | Material Cost | Transport Cost | Construc tion Cost | Total |  |  | 
1 | Thaton | 20 | 1646 | 1711 | 9610 | 16.71 | 419.471 | 22.809 | 67.208 | 509.448 | 2400 | 14 | 209.254 | 5.152 | 11.760 | 226.166 | 735.654 | 13.25 | 624.512
2 | Belin | 20 | 2101 | 2101 | 11882 | 13.48 | 338.388 | 18.400 | 54.217 | 411.005 | 2290 | 20 | 249.948 | 7.360 | 16.800 | 274.108 | 685.113 | 13.59 | 640.537
3 | Kyaik tho | 5 | 2062 | 2062 | 9306 | 4.37 | 109.700 | 5.965 | 17.576 | 133.241 | 860 | 5 | 74.298 | 1.840 | 4.200 | 80.338 | 213.579 | 7.37 | 347.370
4 | Paung | 6 | 1186 | 1417 | 9006 | 4.1 | 102.922 | 5.597 | 16.490 | 125.009 | 1160 | 8 | 110.061 | 2.944 | 6.720 | 119.725 | 244.734 | 9.14 | 430.796
Total |  | 51 | 6995 | 7291 | 39804 | 38.66 | 970.481 | 52.771 | 155.491 | 1178.743 | 6710 | 47 | 643.561 | 17.296 | 39.48 | 700.337 | 1879.080 | 43.35 | 2043.215

## Slide 10
Electrification Plan for Villages of Thaton District
(Within 2 miles from Existing 11 kV Distribution Line)
Kyaiktho Township
No. of Villages - 5 Nos
Househld - 2062 Estimated Cost - 213.579
(mil kyats)
Thaton Township
No. of Villages - 20 Nos
Househld - 1711 Estimated Cost - 735.654
(mil kyats)
Thaton District
No. of Villages - 51Nos
Househld - 7291 Estimated Cost - 1879.080
(mil kyats)
Belin Township
No. of Villages - 20 Nos
Househld - 2101 Estimated Cost - 685.113
(mil kyats)
Paung Township
No. of Villages - 6 Nos
Househld - 1417 Estimated Cost - 244.734
(mil kyats)

## Slide 11: The Statement of Fiscal Yearly Budget and Electrified Connection for Mon State
No | Fiscal Year | State/Region Capital Budget for ESE (mil Kyats) |  |  | State/Region Capital Budget for DRD (mil kyats) | Electrified Connection |  |  | 
 |  |  |  |  |  | On Grid |  | Off Grid | 
 |  | Total Cost for 11 kV Line & 11/0.4 TR | Total Cost for 400 V Line | Total | Off Grid | Village (Nos) | Consumer (Nos) | Village (Nos) | Consumer (Nos)
1 | 2014--2015 Estimate (BE+RE) | 521.41 | - | 521.41 | 738.2 | 24 | 1560 | 29 | 3691
2 | 2015-2016 Estimate (BE+RE) | 2452.81 | 305.53 | 2758.35 | 1400.6 | 50 | 3250 | 68 | 6837
3 | 2016-2017 Budget Estimate (BE) | 1814.46 | 138.8 | 1953.26 | 6768.0 | 21 | 1365 | 173 | 22560
Grand Total |  | 4788.68 | 444.33 | 5233.02 | 8906.8 | 95 | 6175 | 270 | 33088

## Slide 12
 | Dumping site for Material of National Electrification Plan
1 | Mawlamyine District –ESE Compound Mupon ward Mawlamyine township.
2 | Thaton District _Thaton District ESE office, Thaton Township.

## Slide 13
Sr No | Description | Quantities | Transported Site
1 | 11/0.4 kV Distribution Transformer | 34 Nos | Mawlamying District ,PMO Office
2. | 10 meter Concrete Pole | 1210 Nos | Mawlamying District ,PMO Office
3. | ACSR 95mm2 | 61.5 Ton | Mawlamying District ,PMO Office
4. | 11kV Disc Insulators | 960 Set | Mawlamying District ,PMO Office
4. | 11kV Pin Insulators | 3098 Nos | Mawlamying District ,PMO Office
5. | Surge arresters, Disconnectors, Fuses | 34 Set | Mawlamying District ,PMO Office
6. | Other Material | 1 Lot | Mawlamying District ,PMO Office
Main Materials List Transported to Mawlamyine District Office

## Slide 14
Sr No | Description | Quantities | Transported Site
1 | 11/0.4 kV Distribution Transformer | 47 Nos | Thaton District ,PMO Office
2. | 10 meter Concrete Pole | 1760 Nos | Thaton District ,PMO Office
3. | ACSR 95mm2 | 89.8 Ton | Thaton District ,PMO Office
4. | 11kV Disc Insulators | 1389 Set | Thaton District ,PMO Office
4. | 11kV Pin Insulators | 4515 Nos | Thaton District ,PMO Office
5. | Surge arresters, Disconnectors, Fuses | 47 Set | Thaton District ,PMO Office
6. | Other Material | 1 Lot | Thaton District ,PMO Office
Main Materials List Transported to Thaton District Office

## Slide 15
THANK YOU